## Slide 1: 2025 Draft Consolidated RES Model – for Review October 2024
Department of Public Service

## Slide 2: Topics Covered
  Changes to Renewable Energy Standard Under H. 289 (Act 179)
  RES model statutory requirements from 30 V.S.A. § 202b (e)(7)(B)
  Input Assumptions
  Draft Results
  Appendix Slides - What are RECs

## Slide 3: Changes to Renewable Energy Standard Under H. 289 (Act 179)
  In 2024, the Vermont Legislature passed H.289 (Act 179) overhauling the prior law (30 VSA § 8001 - § 8005).
    Full Law Tex available at: https://legislature.vermont.gov/bill/status/2024/H.289
  Summary of changes to law
    Increased overall goal from 75% renewable by 2032 to 100% renewable (date varies by utility)
    Increased Tier II Distributed Generation requirement from 10% to 20%
    Added categories for new regional renewables and load growth
    Changed requirement basis from being based on Retail Sales to being based on “Load” including transmission and distribution line losses

## Slide 4: Changes to Renewable Energy Standard Under H. 289 (Act 179) - Requirements
  Tier I: Total Renewable Energy requirement for utilities changed from 75% to 100% (between 2030-2035, year varies by utility)
  Tier II: In-state distributed renewable energy requirement for utilities changed from 10% to 20% (between 2032-2035, year varies by utility)
  Tier IV: New requirement for utilities to purchase new in-region renewables like offshore wind (quantity and year vary by utility)
  Tier V: Utilities that are already 100% renewable must procure an increasing amount of their new load from new renewables each year based on a 2022 baseline

## Slide 5: Changes to Renewable Energy Standard Under H. 289 (Act 179) - Requirements
Chart: New Renewable Energy Standard Requirements (*)
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Net Tier I | 0.61157 | 0.59408 | 0.54903 | 0.56785 | 0.55036 | 0.73633 | 0.72414 | 0.67066 | 0.66867 | 0.67198 | 0.65884
Tier II | 0.052638 | 0.070126 | 0.087614 | 0.1051 | 0.12259 | 0.14008 | 0.15757 | 0.1766 | 0.17859 | 0.18058 | 0.18151
Tier IV | 0 | 0 | 0.027559 | 0.027559 | 0.027559 | 0.079827 | 0.079827 | 0.11428 | 0.11428 | 0.11428 | 0.15965
Chart: Old Renewable Energy Standard Requirements
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
Net Tier I | 0.54 | 0.534 | 0.528 | 0.562 | 0.556 | 0.55 | 0.584 | 0.578 | 0.572 | 0.606 | 0.6 | 0.594 | 0.628 | 0.622 | 0.616 | 0.65
Tier II | 0.01 | 0.016 | 0.022 | 0.028 | 0.034 | 0.04 | 0.046 | 0.052 | 0.058 | 0.064 | 0.07 | 0.076 | 0.082 | 0.088 | 0.094 | 0.1
*Requirements under new law are approximate and vary by utility. Each utility’s share of the overall RES requirements are based on their 2023 proportional percentage of statewide load

## Slide 6: RES model statutory requirements from 30 V.S.A. § 202b (e)(7)(B)
Sec. 7. 30 V.S.A. § 202b (e)(7)(B)
(B) Projections, looking at least 10 years ahead, of the impacts of the RES
(i) The Department shall consider at least three scenarios based on high, mid-range, and low energy price forecasts.
(ii) The Department shall provide an opportunity for public comment on the model during its development and make the model and associated documents available on the Department’s website.
(iii) The Department shall project, for the State, the impact of the RES in each of the following areas: electric utility rates, total energy consumption, electric energy consumption, fossil fuel consumption, and greenhouse gas emissions. The report shall compare the amount or level in each of these areas with and without the program.

## Slide 7: Load Forecasts
  From VELCO 2024 Long Range Transmission Plan
  Business as Usual (BAU) Scenario: “Continued Growth”
  Policy Scenario: “VT Roadmap” forecast reflects a state statute consistent uptick in the rate of adoption of electric vehicles and cold-climate heat pumps to achieve VT climate goals
Chart: VELCO 2024 Long Range Transmission Plan Statewide Load Forecast
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
BAU (Continued Growth) | 6071698.8867 | 6114967.8153 | 6163671.8652 | 6225730.3239 | 6273575.0956 | 6335843.3003 | 6409069.6047 | 6507710.9787 | 6596559.2138 | 6698574.1219 | 6802705.1635
Policy (VT Roadmap) | 6159986.0799 | 6269324.5508 | 6397255.5762 | 6539584.3123 | 6681807.0929 | 6832361.407 | 6986003.7232 | 7150575.5697 | 7289662.1653 | 7438434.6377 | 7566061.317
https://www.velco.com/sites/default/files/2024-09/101252_Velco_CC24_singles.pdf

## Slide 8: Tier I REC Price
Chart: Tier I REC Prices
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
 | 6 | 6 | 6 | 6 | 7.125 | 7.125 | 7.125 | 7.125 | 7.125 | 7.125 | 7.125
  Average of other New England markets for existing resources
  Maine Existing = ~$3.50
  Massachusetts Clean Energy Standard Existing = ~$9.50

## Slide 9: Tier II REC Price
Chart: Tier II REC Prices
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
 | 45.8844 | 45.8844 | 44.6019 | 44.1744 | 42.4645 | 41.6095 | 39.8995 | 43.5027 | 43.5027 | 43.5027 | 43.5027
  Starts at 2023 Compliance Year actual average Tier II costs then follows trend in regional Class I (Tier IV) REC price forecasts
  2023 Actual = $45.88/REC
  (from Docket # 24-0775-INV)

## Slide 10: Tier IV REC Price
Chart: Tier IV REC Prices
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
 | 40.25 | 40.25 | 39.125 | 38.75 | 37.25 | 36.5 | 35 | 38.1607 | 38.1607 | 38.1607 | 38.1607
  Actual trading price for Nepool Class I RECs through 2031, then an average for remainder of model period

## Slide 11: Tier V REC Price
Chart: Tier V REC Prices
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
 | 40.25 | 40.25 | 39.125 | 38.75 | 37.25 | 36.5 | 35 | 38.1607 | 38.1607 | 38.1607 | 38.1607
  Both Tier II and IV resources qualify for Tier V. Price assumed to match Tier IV as these are expected to be the least-cost resource

## Slide 12: Tier III Incentives
  Tier III incentives based on Actual 2023 costs from docket #24-0775-INV
  Assumed to escalate at inflation (2.93%) for study period
Technology | $/MWhe
Cold Climate Heat Pump | $ 26.00
Electric Vehicle | $ 56.00
Weatherization | $ 25.00
Custom Projects | $ 16.00

## Slide 13: Tier III Technology Allocations
  Allocation of savings assumed to be constant throughout the study period as a simplifying assumption.
  Volume and price of “Custom” projects difficult to predict and therefore not included in model
Cold Climate Heat Pump | 56%
Electric Vehicle | 46%
Weatherization | 2%
Tier II RECs | 2%

## Slide 14: Energy Price Forecasts
  Model uses wholesale price forecast trend to escalate the portion of current statewide cost-of-service tied to energy markets
  Low: 10% discount on New England Avoided Energy Supply Cost Study 2024 – Vermont Counterfactual #1
  Mid: New England Avoided Energy Supply Cost Study 2024 – Vermont Counterfactual #1
  High: New England Avoided Energy Supply Cost Study 2024 – Vermont High Gas Price Sensitivity
Chart: Energy Price Scenarios
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Low | 58.6394 | 46.4631 | 44.6064 | 44.434 | 43.857 | 43.1602 | 44.2011 | 42.6026 | 43.3684 | 43.5974 | 43.8695
Mid | 65.1549 | 51.6256 | 49.5626 | 49.3711 | 48.73 | 47.9558 | 49.1123 | 47.3362 | 48.1871 | 48.4416 | 48.7439
High | 63.1512 | 63.7917 | 61.4558 | 61.8507 | 61.3451 | 59.9682 | 61.6211 | 59.8058 | 60.8424 | 60.6171 | 60.9338

## Slide 15: Model Input: Inflation
  Model uses last 10-year Average Core inflation (CPI less food and energy) to escalate the portion of statewide cost-of-service tied to inflation over time
    Current 12-month average 3.3% as of September 2024
    Model assume 2.93% average experience from 2014 - 2024
model assumption = 2.93%
https://www.bls.gov/charts/consumer-price-index/consumer-price-index-by-category-line-chart.htm

## Slide 16: Impacts of the RES

## Slide 17: Request for Feedback
  PSD would like feedback on the model inputs and assumptions described in this presentation
  Any other thoughts stakeholders have based on review of the model itself are also welcome
  Please send feedback or questions directly to: adam.jacobs@vermont.gov
  Thank You!

## Slide 18: APPENDIX

## Slide 19: DRAFT Projected Costs - BAU
Chart: Annual RES Costs - BAU
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Net Tier I | 13597563.9363 | 13093149.8798 | 11576565.3448 | 12452878.7953 | 14171366.9186 | 22773834.0387 | 22558375.31 | 20528932.4775 | 20807416.4491 | 21391351.2712 | 21191087.2894
Tier II | 14664836.028 | 19676141.7409 | 24086164.0068 | 28904994.9954 | 32658487.6793 | 36928925.9278 | 40292558.3005 | 49997014.7274 | 51250550.0947 | 52622900.4721 | 53715700.9116
Net Tier III | 12361790.4082 | 8677919.615 | 4374630.3796 | -532992.3815 | -6101884.1925 | -12038634.623 | -19069856.9233 | -25449235.1113 | -35054555.0791 | -44426532.0196 | -54084814.7052
Tier IV | 0 | 0 | 6645939.7527 | 6648513.4361 | 6440267.661 | 18460541.1895 | 17906477.8202 | 28378973.9852 | 28766425.3888 | 29211294.3192 | 41445298.8906
Tier V | 604082.8081 | 941596.1022 | 1208990.6135 | 1507822.0102 | 1597429.9978 | 1753973.8207 | 1894688.7738 | 2378329.6481 | 2659839.5923 | 2983067.2967 | 3312999.8348
Total | 41228273.1807 | 42388807.338 | 47892290.0975 | 48981216.8555 | 48765668.0643 | 67878640.3538 | 63582243.2813 | 75834015.7268 | 68429676.4458 | 61782081.3397 | 65580272.2212

## Slide 20: DRAFT Projected Costs – VT Roadmap
Chart: RES Cost - VT Roadmap
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Net Tier I | 22402702.2381 | 22091613.0814 | 20754828.463 | 21891008.3524 | 25654291.0104 | 35208623.2056 | 35317401.9895 | 33344135.5049 | 33823134.6654 | 34619653.3339 | 34446478.2832
Tier II | 14878074.0748 | 20172815.6562 | 24998953.6059 | 30362165.077 | 34783629.9549 | 39822918.016 | 43919629.4734 | 54935972.6079 | 56635464.6214 | 58435123.4283 | 59743334.0134
Net Tier III | 12541540.3922 | 8955461.5522 | 4745458.8959 | -122792.4882 | -5678137.5091 | -11705500.7893 | -18986712.0037 | -25714322.5845 | -36069557.9532 | -46258194.8999 | -56914275.527
Tier IV | 0 | 0 | 6897799.8945 | 6983680.9346 | 6859346.6216 | 19907229.8977 | 19518390.1 | 31182392.5086 | 31788924.4971 | 32437694.8768 | 46096025.7966
Tier V | 773597.7135 | 1347704.5296 | 1903544 | 2517604.4148 | 2860018.2934 | 3258696.2522 | 3571262.6982 | 4415204.9431 | 4855891.916 | 5327267.969 | 5731644.9305
Total | 50595914.4186 | 52567594.8193 | 59300584.8592 | 61631666.2906 | 64479148.3711 | 86491966.5822 | 83339972.2575 | 98163382.98 | 91033857.7467 | 84561544.7082 | 89103207.4967

## Slide 21: Renewable Energy Credits (RECs)
  RECs are the tool used for accounting, tracking and assigning ownership of environmental attributes. ​
  One Megawatt-Hour (MWh) of renewable generation = one REC​
  RECs are used throughout U.S. to track renewability​
  Creates fungible commodity that can be traded​; Renewable attributes can be separated from underlying generation​
    Attributes v RECs
  Creates uniform system for ensuring that there is no double counting​
  Value of REC
    Theory is that REC value should represent the difference between the revenues a resource receives from wholesale markets (e.g. energy, capacity, reserves, etc.) and the cost to build​
    Reality is that value is based on supply and demand​
    Different Tier/Class eligibility means different values